# L298N Dual H Bridge Truth Table
ENA / ENB	IN1 / IN3	IN2 / IN4	Motor State
0	-	-	Off
1	0	0	Fast Stop
1	0	1	Reverse
1	1	0	Forwards
1	1	1	Fast Stop

# Chassis Information
Chassis number	1	2	3	4	5	6	7
Chassis name
Drive wheel teeth	20	20	20	20	20	20	20
20 teeth worth of drive track	16.2cm	16.2cm	16.2cm	16.2cm	16.2cm	16.2cm	16.2cm
Left Motor no load RPM forward
Left Motor no load RPM reverse
Left Motor pulses for 10 revolutions
Right Motor no load RPM forward
Right Motor no load RPM reverse
Right Motor pulses for 10 revolutions

# Pins
D0	Serial Rx	-
D1	Serial Tx	-
D2 (Interrupt pin)	Right hall effects	Input (requires internal pull ups to be enabled)
D3 (Interrupt pin)	Left hall effects	Input (requires internal pull ups to be enabled)
D4	Ultrasonic Forward Trigger	-
D5	Ultrasonic Forward Echo	-
D6 (PWM)	Servo	Analogue Output
D7	IN4	Output
D8	IN3	Output
D9	ENB	Output
D10	ENA	Output
D11	IN2	Output
D12	IN1	Output
D13	Ultrasonic Down Trigger	-
A0 / D14	Left LED	Output
A1 / D15	Right LED	Output
A2 / D16	Right LDR	Analogue Input
A3 / D17	Ultrasonic Down Echo	-
A4 / D18	I2C SDA	-
A5 / D19	I2C SCL	-
A6	Middle LDR	Analogue Input
A7	Left LDR	Analogue Input